## Slide 1: USDW Search
Utilizing the DNR website and SONRIS to perform an unofficial USDW search
Office of Conservation
Injection and Mining Division

## Slide 2: Underground Source of Drinking Water Definition
An Underground Source of Drinking Water is defined by the United States Environmental Protection Agency as:
An aquifer or its portion which supplies any public water system; or
An aquifer or its portion which contains a sufficient quantity of ground water to supply a public water system; and
  Currently supplies drinking water for human consumption; or
  Contains fewer than 10,000 mg/l total dissolved solids and which is not an exempted aquifer.

## Slide 3: Determining the Base of the USDW Using an Electric Log
The IMD typically uses the deep induction curve on an e-log to define the base of the USDW. The following guidelines are used:
  Ground surface to 1,000 feet: 3 ohms or greater is considered USDW;
  1,000 feet to 2,000 feet: 2 ½ ohms or greater is considered USDW; &
  2,000 feet and deeper: 2 ohms or greater is considered USDW
The base of the USDW is established at the base of the sand unit that contains the lowermost USDW with an isolating shale beneath it.
100 feet of net shale must exist between the top of the zone and the base of the USDW.

## Slide 4
USDW ≥ 3 ohms from 0’ – 1000’
Determining USDW on Electric Logs – Example
Base of a Sand Unit Confined by > 30 - 40’ of Shale

## Slide 5
USDW at
515 FEET
Determining USDW on Electric Logs – Example #1

## Slide 6
  Resistivity Curve
    Ground surface to 1,000 feet: 3 ohms or greater
    1,000 feet to 2,000 feet: 2 ½ ohms or greater
    2,000 feet and deeper: 2 ohms or greater
  Establish at the base of the sand unit
  100 feet of net shale between USDW & Top of Zone

## Slide 7
USDW ≥ 2 ½ ohms from 1000’ – 2000’

## Slide 8
USDW ≥ 2 ohms 2000’ and Deeper
2000’

## Slide 10
USDW ≥ 2 ohms 2000’ and Deeper

## Slide 12
BASE OF THE USDW AT 2320’

## Slide 13
20’ (20’ OF NET SHALE)
40’ (60’ OF NET SHALE)
10’ (70’ OF NET SHALE)
15’ (85’ OF NET SHALE)
50’ (135’ OF NET SHALE)
  100 feet of Net Shale between USDW & Top of Zone

## Slide 14
325 ft.
BASE OF THE USDW AT 2320’
SHALLOWEST POSSIBLE TOP OF ZONE

## Slide 15
  Resistivity Curve
    Ground surface to 1,000 feet: 3 ohms or greater
    1,000 feet to 2,000 feet: 2 ½ ohms or greater
    2,000 feet and deeper: 2 ohms or greater
  Establish at the base of the sand unit
  100 feet of net shale between USDW & Top of Zone

## Slide 16
USDW ≥ 3 ohms from 0’ – 1000’

## Slide 18
USDW ≥ 2 ½ ohms from 1000 ’ – 2000’
1000’

## Slide 19
USDW ≥ 2 ohms 2000’ and Deeper
2000’

## Slide 20
  USDW should be established at the base of a sand unit.

## Slide 21
BASE OF THE USDW AT 1405’

## Slide 22
20’ (20’ OF NET SHALE)
25’ (45’ OF NET SHALE)
  100 feet of Net Shale between USDW & Top of Zone

## Slide 23
10’ (55’ OF NET SHALE)
45’ (100’ OF NET SHALE)

## Slide 24
SHALLOWEST POSSIBLE TOP OF ZONE
400 ft.

## Slide 25: SONRIS & Discoverer
Using the DNR database (SONRIS)
to define the base of the USDW

## Slide 26: Identifying the Coordinates of an EXISTING well

## Slide 27: Go to www.dnr.louisiana.gov & click on the SONRIS logo

## Slide 28: Select Data Access (NEW) from Left Menu

## Slide 29: Scroll down to Conservation and select Well Information

## Slide 30: Scroll down to Wells by Serial Number and select Lite link

## Slide 31: Enter the Serial Number of the well & click Submit Query

## Slide 32: Scroll down to WELL SURFACE COORDINATES & Locate the Lambert X, Lambert Y, Zone, and Datum fields

## Slide 33: USDW Search in Discoverer

## Slide 34: Select Data Access (NEW) from Left Menu

## Slide 35: Scroll down to Conservation and select Injection Information

## Slide 36
Scroll down to UIC Appl: USDW Search By Lambert X/Y Coordinates & select ROD link

## Slide 37
Enter the location’s X,Y Coordinates (do not use commas)

## Slide 38
Select the flashlight icon next to the Surface Coordinates Zone field and choose the appropriate Zone- N (North), S (South), O (Offshore)

## Slide 39
Select the flashlight icon next to the Surface Coordinates System field and choose the System/Datum- 1927 or 1983

## Slide 41: Modifying the Search Criteria If No Wells are Retrieved in a 1-mile AOR - or – If a USDW Value cannot be identified from the Wells that are Retrieved

## Slide 42
Click on the 10th Icon from the left. When you mouse-over the icon, it will say Refresh.

## Slide 43
Increase the distance in the Radius (ft) field and select the OK button.
If a well with an electric log cannot be identified within 2 MILES of the proposed location, please contact IMD.

## Slide 44: USDW Search Exporting Spreadsheet to EXCEL

## Slide 45
Select File from the Menu bar & Select Export from the dropdown menu

## Slide 46
Click on the Next button

## Slide 47
Click on the Browse button to select the location where you want to save the spreadsheet

## Slide 48
Click on the Location dropdown menu and select the appropriate drive

## Slide 49
Enter a File Name that is easily identifiable, and click on the Save button.

## Slide 50
Click on the Next button.

## Slide 51
Click on the Finish button.

## Slide 52
The Export is Complete. Select the OK button

## Slide 54
BOLD the Header Row & Apply Word Wrap
Center the values in the Columns
Expand the Column Width

## Slide 55
Distance from Lambert X/Y (Feet) Column Provides the distance of the well from the X/Y coordinate values that were searched. The table is sorted by this Column from closest to farthest. If the search was conducted based on the coordinates of an existing well, then the well in the first row should be the well itself.

## Slide 56
Locating the Most Accurate USDW Value Although a USDW Value may be confirmed for a well in the AOR, you must search the electric logs of all wells closer to the proposed well to find the most accurate USDW Value.

## Slide 57
Log Reviewed Flag Column Indicates whether the log has been recently reviewed by an IMD Geologist.
  This field was recently added at the request of IMD Geologists so that we could keep track of wells whose electric logs we have reviewed.

## Slide 58
Area USDW Value Column If a value is present, it indicates that a USDW value was determined from an electric log of an offset well. The SN, and sometimes the distance to the well, are usually indicated in the Source Area USDW field.
“0” DOES NOT indicate that a USDW is not present at the wellbore or that a USDW is at the ground surface. It is a default value entered by SONRIS.

## Slide 59
USDW Value Column If a value is present, then it indicates that the value was determined from the electric log of the well itself.
“0” DOES NOT indicate that a USDW is not present at the wellbore or that a USDW is at the ground surface. It is a default value entered by SONRIS.

## Slide 60
Source Area USDW Value Column If an entry is present, then it may be in one of the following formats:
  USDW VALUE PER LCB XX/XX/XXXX Indicates the Geologist from IMD who identified the value in the USDW Value field and the date it was identified.
USDW VALUE PER LCB 10/07/1999

## Slide 61
Source Area USDW Value Column If an entry is present, then it may be in one of the following formats:
  FROM ELOG OF SN: XXXXX (~XXX’ AWAY) PER H BORDEN XX/XX/XXXX Indicates the SN of offset well whose elog was used to determine the value indicated in the Area USDW Value field, the distance of the offset well, the Geologist from IMD who identified the value, and the date it was identified.
FROM ELOG OF SN 121587 (~939’ AWAY) PER H BORDEN 11/13/2008

## Slide 62
Source Area USDW Value Column If an entry is present, then it may be in one of the following formats:
  NO LOG FOUND Means a search was conducted for a log with that Serial Number, but none was found.
NO LOG FOUND

## Slide 63
Source Area USDW Value Column If an entry is present, then it may be in one of the following formats:
  TOL @ XXX’ Is entered when a USDW is not present on the log, and indicates the shallowest depth the log was recorded.
TOL@1802’

## Slide 64
Source Area USDW Value Column If the USDW Value field contains a value and the Source Area USDW Value field is blank, then it indicates that the USDW Value was determined from an electric log of the well, but it has not been recently confirmed by current standards. The e-log of the well will need to be reviewed.
  If the USDW Value or Area USDW Value fields are blank or contain “0” and the Source Area USDW Value field is blank, then it indicates that a search has not been conducted to identify a USDW for the well.

## Slide 65: Electric Log Search

## Slide 66: Go to www.dnr.louisiana.gov & click on the SONRIS logo

## Slide 67: Select Document Access from Left Menu

## Slide 68: Select Document Type from Left Menu

## Slide 69: Scroll down and select Well Log

## Slide 70: Enter the Well Serial Number in the field to the right and select the Search button
100100

## Slide 71: If an electric log is available, a table will show the well log information. Click on the TIF image and Save to your computer

## Slide 72: Viewing and Printing Electric Logs

## Slide 73: Download a Log Viewing Software
Example provided is Blueview by Schlumberger

## Slide 74: Go to www.slb.com and enter BlueView Log Image in the search field at the top of the page

## Slide 75: Select the first result BlueView Log Image Manipulation Software, Schlumberger

## Slide 76: Click on the BlueView Log Image Manipulation Software link under the Related Resources heading

## Slide 77: Save the blueview_software.zip file to your computer

## Slide 78: Double click on the executable file and follow the download instructions to install BlueView to your computer

## Slide 79: Viewing a Log

## Slide 80: Once downloaded, locate the Blueview icon on your desktop and double-click to open.

## Slide 81: Select File from the top menu, and choose Open Image File(s) from the drop down menu.

## Slide 82: Locate the Elog saved to your computer and Open it in Blueview

## Slide 83: Make sure the FIT button is selected in the menu bar. Scroll down to view the entire log.

## Slide 84: Printing a Log

## Slide 85: To print the log, select File from menu bar, and choose Print Preview from the drop-down menu.
Print Ctrl+P

## Slide 86: Previewing large images takes a lot of memory. The program will ask if you want to view the ENTIRE IMAGE (Yes), or ONLY 3 PAGES (No). Select No.

## Slide 87: Preview the log. If the elog width does not fit on the page, adjust the size of the image by selecting the Scale by Percentage button from the menu bar.

## Slide 88: Enter a new Percentage in the Scale By (%) field, and select the Print Preview button from the menu bar.

## Slide 89: Preview Only 3 Pages by selecting the No button.

## Slide 90: When you are ready to Print, select File from the menu bar, and choose Print from the drop-down menu

## Slide 91: Select the name of the Printer, select the Preferences button to adjust the printer settings, under the Page Range section choose All, and when ready click the Print button.

## Slide 92: Select the Close button to return to the main screen.

## Slide 93: IMD Contact List
Teresa Rougon, Geologist Supervisor
(225) 342-5581 teresa.rougon@la.gov
Luzma Mata de Leder, Geologist
(225) 342-8639 maria.leder@la.gov
Kathy McGillis, Geologist
(225) 342-9054 kathy.mcgillis@la.gov

## Slide 94
Source Area USDW Value Column If an entry is present, then it may be in one of the following formats:
  DUAL COMP; TOL@1839’ FROM ELOG OF SN XXXXX Is entered when the well is a dual completion and the electric log of the well is filed under the Serial Number of the original completion, followed by the Source Area USDW information for the original well.
DUAL COMP; TOL@1839’ FROM ELOG OF SN 69799
The field is blank because is it the same distance away as the well above it.

## Slide 95
Distance from Lambert X/Y (Feet) Column Provides the distance of the well from the X/Y coordinate values that were searched. The table is sorted by this Column from closest to farthest. If the search was conducted based on the coordinates of an existing well, then the well in the first row should be the well itself.
Log Reviewed Flag Column Indicates whether the log has been recently reviewed by an IMD Geologist.
Area USDW Value Column If a value is present, it indicates that a USDW value was determined from an electric log of an offset well. The SN, and sometimes the distance to the well, are usually indicated in the Source Area USDW field.
USDW Value Column If a value is present, then it indicates that the value was determined from the electric log of the well itself.
USDW Search Results USDW Value defined in SONRIS within 1-mile Radius

## Slide 96
Source Area USDW Value Column If an entry is present, then it may be in one of the following formats:
  USDW VALUE PER LCB XX/XX/XXXX, Indicates the Geologist from IMD who identified the value in the USDW Value field and the date it was identified.
  FROM ELOG OF SN: XXXXX (~XXX’ AWAY) PER LCB XX/XX/XXXX, Indicates the SN of offset well whose elog was used to determine the value indicated in the Area USDW Value field, the distance of the offset well, the Geologist from IMD who identified the value, and the date it was identifiedThe SN is usually indicated in the Source Area USDW field.
  NO LOG FOUND, Means a search was conducted for a log with that Serial Number, but none was found.
  TOL @ XXX’, Is entered when a USDW is not present on the log, and indicates the shallowest depth the log was recorded.
USDW Search Results USDW Value defined in SONRIS within 1-mile Radius