## Slide 1
Ground Water Resources Commission Meeting
Wednesday, February 3, 2010

## Slide 2
Mr. John Adams
DNR Office of Conservation
Adoption of Minutes
December 2, 2009

## Slide 3
Mr. Gary Hanson
Water Resources Committee of Northwest Louisiana
Update on NW Louisiana Water Resources Issues

## Slide 4
LSU Shreveport Red River Watershed Management Institute
Gary Hanson, Director
Amanda Lewis, Assistant to Director
Update of Northwest Louisiana Water Resource Issues
Louisiana Ground Commission Meeting
Shreveport - February 3, 2010

## Slide 5
Water Resources Committee of Northwest
Red River Watershed Management Institute
Water Issues - Haynesville Shale Play
TOPICS TO BE COVERED:

## Slide 9: Haynesville Shale - A Resource Play
Haynesville Shale
Haynesville Shale Discovery, Development, and Impact on Local Water Utilities

## Slide 10
Haynesville Shale Discovery, Development, and Impact on Local Water Utilities
Development of an unconventional resource play, like the Haynesville Shale, has one thing in common with other domestic gas shale plays, large amounts of water are needed for well stimulation. As the play exploded in northwest Louisiana, the gas industry encountered a public that was already aware of groundwater concerns. Gas operators, local government, state and federal regulators, and the general public are learning to deal with surface and groundwater issues as Haynesville development moves forward.
LSUS Red River Watershed Management Institute, 2010

## Slide 11
Haynesville Shale
LSUS Red River Watershed Management Institute
AAPG, 2007
Haynesville Shale
Marcellus Shale
Eagleford Shale
Barnett Shale
Fayetteville Shale
Woodford Shale

## Slide 12
Haynesville Shale
LSUS Red River Watershed Management Institute
AAPG, 2007
Haynesville Shale
Marcellus Shale
Eagleford Shale
Barnett Shale
2074 trillion cubic feet of total U.S. future supply = 350 billion barrels of oil which is the same as the oil reserves of Saudi Arabia!

## Slide 13
Structure Map – Top of Cotton Valley Group
Generalized structure contours on top of Cotton Valley Group sandstone across northeastern Texas and northern Louisiana, modified from Finley (1984).
+7 TCF
8 TCF
Monroe Fld.
Carthage Fld.

## Slide 14: Louisiana Haynesville Shale Activity Map - 2008
LADNR, 2008
Notes: 14
14

## Slide 15: Louisiana Haynesville Shale Activity Map - 2009
LADNR, 2009
Notes: 15

## Slide 16
Structure Map – Top of Cotton Valley Group
Generalized structure contours on top of Cotton Valley Group sandstone across northeastern Texas and northern Louisiana, modified from Finley (1984).
Haynesville Play
8 TCF
Monroe Fld.
Haynesville
Shale Play
>250 TCF!

## Slide 17
Ewing, 2009
Generalized Haynesville Depositional System

## Slide 18
"Gorilla Uplift" - Sabine Uplift
Boundaries of the Sabine Uplift based on Wilcox outcrop
Gorilla Uplift
After Ewing, 2009
Also only source of groundwater
(Wilcox Recharge Area)

## Slide 19
Haynesville Top Drive Rig Drilling & Adjacent Well Being Hydraulically Fraced
AQUAPURE, 2008
Frac job underway

## Slide 20
This year’s theme, A Fusion of Geology & Technology, illustrates the critical interdependency of the geosciences and petroleum technologies that we utilize to explore for and develop hydrocarbon resources. The color infrared (CIR) aerial imagery was acquired along the Red River at Shreveport and Bossier City and represents the ever increasing role that surface and groundwater resources play in drilling and development of unconventional resource plays like the Haynesville Shale. Just as the river runs through above, the drill stem serves to connect the subsurface geology with applied
technologies utilized below.
Gulf Coast Association of Geological Associations Shreveport - 2009

## Slide 21
Haynesville
(Typical Productive Zone)
Haynesville Shale - Sabine Uplift
HS-04
Lower Cotton Valley Bossier Shale
(New Developing Play)
Vertical Well - Left
Horizontal Well has been drilled to TD 14,550'
LSUS Red River Watershed Management Institute, 2010

## Slide 22
Hydraulic Fracturing (Fracing a Well)

## Slide 23
Fracing a Well
1. "Slick water" frac (surfactant & biocide added to water) or gel frac
2. Frac sand or high strength proppant
3. Pumped under high pressure
AQUAPURE, 2008
Scale?

## Slide 24
Fracing a Well
1. "Slick water" frac (surfactant & biocide added to water) or gel frac
2. Frac sand or high strength proppant
3. Pumped under high pressure
AQUAPURE, 2008
Scale?

## Slide 25
Hydraulic Fracturing in Haynesville Shale Geologic Risk = Very Low
Realistic scale drawing for Haynesville

## Slide 26
1. "Slick water" frac (surfactants & biocide added to water) or gel frac
2. Frac sand or high strength proppant
3. Water & proppant are pumped under high pressure
Fracing a Haynesville Well
11,000 ft. -12,000 ft.
Scale?
Al Grandberg, 2008

## Slide 27
U. S. Major Shale Gas Plays
Average Natural Gas Well vs Haynesville Gas Well
Average U.S. natural gas well - 500 mcfg/d
Average Barnett Shale gas well - 1,000 mcfg/d
Average Haynesville gas well - 10,000 mcfg/d*
Haynesville Shale is overpressured - .85 - 1.0
Other shale plays normal pressure - .46
Flow rates Cumulative Production
mcfg/d = 1000 cu. feet gas/day BCF = 1,000,000,000 cubic feet gas
mmcfg/d = 1,000,000 cu. feet gas/day TCF = 1,000,000,000,000 cubic feet gas
* 10 million ft3 gas per day

## Slide 28: What are the water usage Issues?
Unconventional resource plays either require or discharge large volumes of water
Older plays (Barnett) should be "mined" for water usage "lessons learned" that can be utilized in newer plays (Haynesville, Marcellus)
Water sourcing, hydraulic fracturing (Fracking) as well as water disposal are issues of concern

## Slide 29
Marcellus Shale operators are confronted with severe restrictions on the disposal of flowback/produced water due to the lack of treatment/disposal facilities
Gas well development is a new concept for the public in many areas of the Marcellus Shale
Haynesville Shale operators encountered a public that was aware of existing groundwater problems
What are the water usage issues?

## Slide 30
What are the water usage issues?

## Slide 31: Understanding Water Resources
Water Resources and Man
The people of northwest Louisiana are well accustomed to oil and gas development

## Slide 32
Water and Culture - More than just a commodity

## Slide 33
Water and Culture - More than just a commodity
The community became wary of gas exploration operations

## Slide 34
Who’s on first…?

## Slide 35
Groundwater
  Carrizo-Wilcox Aquifer
    Initially the main source for fracing
Water Sources for Haynesville Play
LSUS Red River Watershed Mangement Institute
How and where do you get the water? ...Approaches

## Slide 36
Groundwater
  Carrizo-Wilcox Aquifer
    Initially the main source for fracing
Water Sources for Haynesville Play
LSUS Red River Watershed Mangement Institute
How and where do you get the water? ...Approaches

## Slide 37
Louisiana Aquifers
Carrizo-Wilcox

## Slide 38
Rural parish withdrawals are predominantly groundwater from Carrizo-Wilcox Aquifer
Source USGS
7.7 million gallons/day
Caddo Parish Water Use - 2005

## Slide 39
Gas Industry
Use
G. Hanson
LSUS Red River Watershed Management Institute - Shale Gas Plays
< 1,000,000 gallons
7,000,000 gallons
What are the choices for industry water usage?

## Slide 40
Parishes Overlying Carrizo-Wilcox Aquifer
LSUS Red River Watershed Management Institute

## Slide 41
Generalized Geologic Cross-section Northwest Louisiana
LSUS Red River Watershed Management Institute
Carrizo-Wilcox Aquifer

## Slide 42
Updip Pinch-out of Carrizo-Wilcox Northern Caddo Parish, Louisiana
G. Hanson
Wilcox Group
Midway Group

## Slide 43
Thin Sands
Intermediate Sands
Thick Sands
LSUS RRWMI, 2008 and USGS, 1993
Carrizo-Wilcox Aquifer
A Poor Aquifer...

## Slide 44
Sand & Shale
Sand & Shale
Carrizo-Wilcox Aquifer
NW Louisiana & NE Texas
Midway shale
After USGS, 1993
Sands are lenticular channel deposits
Why is the Carrizo-Wilcox Aquifer such a poor aquifer?
LSUS Red River Watershed Management Institute

## Slide 45
LSUS RRWMI, 2008 and USGS, 1993
Caddo Parish / LSUS Monitoring Well
Cone of Depression
Long Term Consequences of Excessive Groundwater Withdrawal - Carrizo-Wilcox Aquifer
Southern Trace Golf Course

## Slide 46
Long Term Consequences of Excessive Groundwater Withdrawal - Carrizo-Wilcox Aquifer
Groundwater Recharge Potential - Caddo Ph./LSUS Monitoring Wells

## Slide 47
Water and Culture - More than just a commodity
Professional waterworks administrators became convinced that the withdrawal of excessive amounts of groundwater by gas operators was depleting the aquifer.
The Times
Initially some water districts provided water to gas companies for fracing

## Slide 48
RED RIVER WATERSHED MANAGEMENT INSTITUTE (RRWMI)
Develop courses that address watershed & floodplain issues
Help coordinate state & federal funded watershed projects
Focus research efforts on finding solutions to watershed related problems
Develop and coordinate community outreach projects
Work with industry partners to jointly develop approaches that enhance economic development and preserve natural resources
Goals and Objectives:

## Slide 49
Walter B. Jacobs Memorial Park. LSUS students were involved in all phases of planning, drilling and development of the monitoring wells in the joint Caddo Parish & LSUS project.
Drilling of the project’s first groundwater monitoring well at Walter B. Jacobs Memorial Park. LSUS students observe drilling operations.
LSUS/Caddo Parish Monitoring Well Project
LSUS Red River Watershed Management Institute
M. Hanson
M. Hanson

## Slide 50
Wilcox Aquifer
Midway Shale
Electric Log of Walter B. Jacobs Park Monitoring Well
LSU Shreveport Student Collecting Groundwater Sample

## Slide 51
Continuous Groundwater Monitoring (preliminary data)
LSUS/Caddo Parish Monitoring Well Project
(Background well)

## Slide 52
1
3
4
5
Walter Jacobs Park
Hannah’s Park
Mayo Road
Keithville
Springridge
Monitoring Well Sites
2
1
2
4
3
5
SHREVEPORT
Caddo Parish/ LSUS Monitoring Well Project
Red River Watershed Management Institute LSU Shreveport
Water Resources Committee of Northwest Louisiana
Phase II Wells (2009-10)

## Slide 53
1
Water Levels
(Monthly)
Caddo Ph./LSUS Monitoring Wells
2
3
4
5

## Slide 54
1
3
4
5
Walter Jacobs Park
Hannah’s Park
Mayo Road
Keithville
Springridge
Monitoring Well Sites
2
1
2
4
3
5
SHREVEPORT
Caddo Parish/ LSUS Monitoring Well Project
Red River Watershed Management Institute LSU Shreveport
Water Resources Committee of Northwest Louisiana
Phase II Wells (2009-10)

## Slide 55
1
Water Quality
Quarterly
Caddo Ph./LSUS Monitoring Wells
2
3
4
5

## Slide 56
1.5 Years of Data

## Slide 57
LSUS Red River Watershed Management Institute
LSU Shreveport and Red River Education & Research Park
Red River Education & Research Park
LSU Shreveport
Red River
Anderson Watershed Research Station

## Slide 58: LSUS Surface Water Monitoring Station

## Slide 59
Groundwater
  Carrizo-Wilcox Aquifer
  Red River Alluvial Aquifer
    Not in competition with public use
Water Sources for Haynesville Play
LSUS Red River Watershed Management Institute

## Slide 60
Magnetic Resonance Imaging Log (MRIL)
Red River Alluvial Aquifer
Wilcox Aquifer
LSUS 001 Monitoring Well Project - Wilcox/Alluvial Aquifer
Halliburton Logging Well
LSUS Red River Watershed Management Institute
LSUS Research Park

## Slide 61
Monitoring Well Instrumentation
Surface water - ground water interaction

## Slide 62
Red River Alluvial Aquifer
LSUS RRWMI, 2008

## Slide 63
Red River Alluvial Aquifer near Dixie, La.
West
East
Red River Alluvial Aquifer
Floodplain
After USGS, 1993
Sand
Red River Alluvial Aquifer

## Slide 64
The Times (Shreveport) - This article is a good example of how the press can inform and educate the public
Vickie Welborn, 2009

## Slide 65
Office of Conservation recommends that operators use the Red River Alluvial Aquifer for fracing wells

## Slide 66
Gas Industry
Use
Water Loss
Main source of frac water at start of Haynesville Play
G. Hanson
LSUS Red River Watershed Management Institute - Shale Gas Plays
< 800,000 gallons
7,000,000 gallons
Do operators use
the 800 pound Gorilla Approach?

## Slide 67
Gas Industry
Use
Water Loss
Main source of frac water at start of Haynesville Play
G. Hanson
LSUS Red River Watershed Management Institute - Shale Gas Plays
< 800,000 gallons
7,000,000 gallons
The 800 pound Gorilla Approach
Can we work together to find alternative sources?
OR

## Slide 68
Surface Water Sources – South Caddo, Desoto
Red River
Clear Lake (small)
Toledo Bend Reservoir
Sabine River
LSUS Red River Watershed Management Institute

## Slide 69
Water Resources Committee of Northwest Louisiana
Established prior to Haynesville in 2003
Members: Bossier, Caddo, Desoto, & Webster Parish Administrators, Shreveport, MPC, LSUS, Sabine River Authority, local mayor, Red River Valley Authority, Red River Waterway Commission, community representatives, an oil & gas co.
Dedicated to insuring the supply of good quality water surface & groundwater for Northwest La.

## Slide 70
Water Resources Committee of Northwest Louisiana (WRCNL)
Sabine River Authority (Member)
LSUS Red River Watershed Management Institute

## Slide 72
Recent Article in "The Land Rig"

## Slide 74
Alternate Water Sources for Frac Water
The Times
LSUS Red River Watershed Management Institute

## Slide 75
Get Rich Quick ?– Don’t sell the farm, just sell the pond water…
Private ponds have become an important source of frac water
Alternate Water Sources for Frac Water

## Slide 76
You guys seen any unleased ponds?
A Whole New Type of Lease Market…
Notes: 76

## Slide 77
Water Sources for Haynesville Play
Surface runoff ponds frac water

## Slide 78
Water Sources for Haynesville Play
Groundwater ponds frac water
"Industrial Water Well"

## Slide 79
Gas Industry
Use
Water Loss
La. Office of Conservation Commissioner states drilling domestic wells to supply ponds for frac water may be illegal
G. Hanson
LSUS Red River Watershed Management Institute - Shale Gas Plays

## Slide 80
LSUS Red River Watershed Management Institute
As the gas industry started to move from groundwater to surface water for frac supply water, surface water sources began to dry up. Initially small bayous, streams and private ponds were used.
Initial contact with US Corps of Engineers led to the understanding that the Red River could be used without any permits.
As natural gas operators started to use the river, the Corps informed them and me that a Section 10 permit was required for withdrawal.
Initially operators were met with delays with no permits issued.
From Groundwater to Surface Water The Start

## Slide 81
LSUS Red River Watershed Management Institute
The Executive Director of the Red River Waterway Commission (Ken Guidry) and I set up a meeting at LSUS that included Vicksburg Division Corps managers, several gas operators, Louisiana Oil & Gas Assoc., a local levee district board president and a water transport company.
The goals of this first meeting included 1) educating the non-industry participants about natural gas drilling & completion operations, 2) informing them about surface water pumping & transportation, 3) developing a protocol for permitting withdrawal sites on the river.
From Groundwater to Surface Water Organization - Better
1st Meeting

## Slide 82
Needless to say, some of the parties we invited to the first meeting were a little skeptical…

## Slide 83: The first order of business was to find common ground on terminology
1 Acre-foot = 325,848 gallons (lakes & rivers)
1 Barrel = 42 gallons (Gas industry), Gallons/minute (gpm)
Toledo Bend Reservoir
    4,476,951 Acre-feet @ 172 ft. msl
    4,200,000 Acre-feet annual average inflow
Red River at Shreveport
  Discharge = 24,900 ft3/sec = 404,000 gallons/minute (gpm)
  24,900 gpm = 962 bbls/m
Oil/Gas Exploration/Development per well
    7.0 million gallons/ 21.5 acre-feet/ 167,000 bbls (14 stages)
Potential 30,000 gas wells in Haynesville Play
    30,000 x 7,000,000 gals. = 210,000,000,000 gals. or 210 Billion gal. or 644,472 acre-feet
Notes: 83
83

## Slide 84
LSUS Red River Watershed Management Institute
A second meeting was called about a month later to provide the Corps with estimated future withdrawal rates/volumes and to finalize a protocol for permit submission. Just prior to the meeting Chesapeake was issued the first permit. Shortly after this meeting several more permits were issued to 2 other operators.
From Groundwater to Surface Water Results
Success!

## Slide 85
LSUS Red River Watershed Management Institute
It was during the second meeting that the relationships among all parties started to jell. Early on, the Corps recognized the need and urgency to help move the operators from the highly stressed aquifers to abundant surface water. It was important to the Corps that 1) water withdrawn would not impair operation of locks; 2) pump equipment in the river would not impair navigation; and 3) levees would not be damaged. They had requested water usage information during the first meeting and Chesapeake responded with estimated water use, and with the other operators contributing, it became obvious to the Corps that the natural gas operators water withdrawal from the Red River would be of minimal impact.
From Groundwater to Surface Water Results

## Slide 86
LSUS Red River Watershed Management Institute
From Groundwater to Surface Water Results
It had been requested of the Corps to provide a clear understanding:
1) for submitting permit requests
2) so operators could determine areas where temporary pump stations could or could not be sited and
3) where Section 10 permits were required.
The operators & Corps representatives developed a good rapport & both sides have developed an understanding of what is needed to withdraw water from the river. The gas operators invited the Corps to visit their operations. The Corps responded with cordial and informative visits. Permits are now flowing & so is the water from the Red.

## Slide 87
LSUS Red River Watershed Management Institute
Water Being Pumped to Haynesville Shale Well
M. Hanson

## Slide 88
The press were also invited to the second meeting. Excellent, informative publicity followed.

## Slide 89
Water and Culture
“They can pull as much as they want” John Neilson
"...cited the permitting process that's shifting some oil and natural gas operators to Red River"
"Positive things are happening...We have gotten some good results because some of the companies are pulling back" G. Hanson

## Slide 90
LSUS Red River Watershed Management Institute
A couple of months after the 2nd meeting one of the operators indicated that the US Fish & Wildlife Service (USFWS) was processing permits slowly. A third meeting was held with the Corps and the USFWS in attendance. As with the Corps in the first meeting, part of the meeting was spent briefing the USFWS about natural gas drilling and completion operations. The USFWS reviewed the need & methodology for threatened & endangered species surveys on the Red River. The USFWS stated that they would insure the permit applications would be reviewed without delay. One of the operators reported after the meeting that they had a permit clear the Corps & USFWS in 19 days!
From Groundwater to Surface Water A Smooth Road

## Slide 91
Utilization of Red River Water As a Source For Natural Gas Well Drilling and Stimulation
Participants:
US Army Corps of Engineers Vicksburg
Red River Waterway Commission
Red River Watershed Management Institute
Caddo Levee District, Bossier Levee District
Louisiana Department of Transportation
Natural Gas Industry Representatives: Camterra, Resources, Chesapeake Energy, Questar Exploration & Production, EnCana, EXCO and Petrohawk Energy
Louisiana Oil and Gas Association
Red River Pump and Impact
Water Resources Committee of Northwest Louisiana
International Paper Company, Mansfield
3rd Meeting - LSUS
LSUS Red River Watershed Management Institute

## Slide 92
LSUS Red River Watershed Management Institute
30 water withdrawal sites
Status of permitted sites:

## Slide 93
City of Shreveport Water Bulk Station South of Town (Surface Water) & Potential Treated Waste Water

## Slide 94
Water Sources for Haynesville Play
Groundwater (Carrizo-Wilcox not preferred)
Surface water (Ponds, Red & Sabine Rivers)
Recycling (Need Office of Conservation Change)
Treated wastewater (City of Shreveport, International Paper Company, Mansfield)

## Slide 95
VS ?
G. Hanson
LSUS Red River Watershed Management Institite
Decrease Water Loss

## Slide 96
G. Hanson
Need for Balance
Decrease Water Loss

## Slide 97
New reporting requirements initiated by Office of Conservation

## Slide 98: New water use reporting guidelines
Groundwater supply well
Total Groundwater Used

## Slide 99
Wellsite Spill Prevention

## Slide 100: Summary
A Water Market has developed in the Haynesville shale play
Operators are hiring individuals whose only job is to find and negotiate terms for the purchase of surface water
Operators & regulators are working together
Operators are cooperating with other operators to conserve groundwater (bartering, etc.)
Office of Conservation has modified water reporting (WH-1 & Reuse of produced water)
Local water districts are providing water for fracing if their water source is surface water

## Slide 101
You may love sausage but not many people want to see how it is made.

## Slide 102
Water Management - Not a Simple Issue!
LSUS Red River Watershed Management Institute

## Slide 103
In order to get this...
Summary
LSUS Red River Watershed Management Institute

## Slide 104
Water Resources Committee of Northwest Louisiana
We are solving this!
Summary
LSUS Red River Watershed Management Institute

## Slide 105
Mr. Jim Broussard
DNR Office of Conservation
Office of Conservation Rules and Process to Protect Groundwater During Oil and Gas Drilling and Production

## Slide 106
Well Construction Requirements
  Multiple casing strings
  Minimum setting depth
  Cement
  Pressure testing
Well Abandonment Requirements
  Cement plug locations/depths
  Plug thickness
  Pressure testing
Both requirements result in protection of USDW and isolation of hydrocarbon bearing zones.
Regulatory Methods

## Slide 107
Well Construction - Casing Types
Conductor Casing or Pipe
  Prevents erosion of unconsolidated surface sediments, protects rig foundation, and may offer structural support for the wellhead.
  Use and removal at discretion of operator.
Surface Casing or First Intermediate Casing
  Supports unconsolidated surface deposits, protects shallow, fresh-water sands from contamination.
  OC Regulations specify minimum depth, cement, and test requirements.
Intermediate Casing
  Protects against caving of heaving formations, abnormally pressured formations, lost circulation zones, unstable shale or salt sections or used to segregate upper oil, gas or water-bearing strata.
  Use and specifications are typically at discretion of operator.
  May be required by District Manager. If required, depth, casing grade, cementing and testing requirements may determined by hearing.
Production Casing
  Segregates the horizon from which production is obtained and affords a means of communication between such horizons and the surface.
  OC Regulations specify cement and test requirements. Casing depth is determined by depth of productive intervals.

## Slide 108
Surface Cement
1860 to surface
Intermed. Cement
10,520 to ~4,000
Prod. Cement
TD to ~6,000
USDW
Max 1,600 ft
~10,700 ft (~2 miles)
From base of USDW to
Top of Haynesville Shale
Haynesville
~12,300 ft
TD:
12,270 ft TVD
16,630 ft MD
SURFACE CSG
INTERMED. CSG
PROD. CSG
WELL CONSTRUCTION EXAMPLE

## Slide 109
Casing Configuration Example
5 in.
Production
7 ⅝ in.
Intermediate
10 ¾ in.
Surface

## Slide 110
Table 1 |  |  | 
Total Depth of Contact | Casing Required | Number of Sacks Cement | Surface Casing Test Pressure (lbs. Per sq. in.)
0-2500 | 100 | 200 or circulate to surf* | 300
2500-3000 | 150 | 500 " | 600
3000-4000 | 300 | 500 " | 600
4000-5000 | 400 | 500 " | 600
5000-6000 | 500 | 500 " | 750
6000-7000 | 800 | 500 " | 1000
7000-8000 | 1000 | 500 " | 1000
8000-9000 | 1400 | 500 " | 1000
9000-Deeper | 1800 | 500 " | 1000
*Circulate to the Surface shall mean the calculated amount of cement necessary to fill the theoretical annular space plus 10 percent. |  |  | 
Casing Program Requirements – Surface Casing Minimum Depth
“Where no danger of pollution of fresh water sources exists, the minimum amount of surface or first intermediate casing to be set shall be determined from Table 1 hereof.” - LAC 43:XIX.109.B.1
“In known low-pressure areas, exceptions to the above may be granted by the commissioner or his agent. If, however, in the opinion of the commissioner, or his agent, the above regulations shall be found inadequate, and additional or lesser amount of surface casing and/or cement or test pressure shall be required for the purpose of safety and the protection of fresh water sands.”- LAC 43:XIX.109.B.1.a

## Slide 111
Table 1 |  |  | 
Total Depth of Contact | Casing Required | Number of Sacks Cement | Surface Casing Test Pressure (lbs. Per sq. in.)
0-2500 | 100 | 200 or circulate to surf* | 300
2500-3000 | 150 | 500 " | 600
3000-4000 | 300 | 500 " | 600
4000-5000 | 400 | 500 " | 600
5000-6000 | 500 | 500 " | 750
6000-7000 | 800 | 500 " | 1000
7000-8000 | 1000 | 500 " | 1000
8000-9000 | 1400 | 500 " | 1000
9000-Deeper | 1800 | 500 " | 1000
*Circulate to the Surface shall mean the calculated amount of cement necessary to fill the theoretical annular space plus 10 percent. |  |  | 
Casing Program Requirements – Surface Casing Cementing
“Cement shall be allowed to stand a minimum of 12 hours under pressure before initiating test or drilling plug. Under pressure is complied with if one float valve is used or if pressure is held otherwise.…”- LAC 43:XIX.109.B.3
12 Hour Standing Time

## Slide 112
Table 1 |  |  | 
Total Depth of Contact | Casing Required | Number of Sacks Cement | Surface Casing Test Pressure (lbs. Per sq. in.)
0-2500 | 100 | 200 or circulate to surf* | 300
2500-3000 | 150 | 500 " | 600
3000-4000 | 300 | 500 " | 600
4000-5000 | 400 | 500 " | 600
5000-6000 | 500 | 500 " | 750
6000-7000 | 800 | 500 " | 1000
7000-8000 | 1000 | 500 " | 1000
8000-9000 | 1400 | 500 " | 1000
9000-Deeper | 1800 | 500 " | 1000
*Circulate to the Surface shall mean the calculated amount of cement necessary to fill the theoretical annular space plus 10 percent. |  |  | 
Casing Program Requirements – Surface Casing Pressure Testing
“Surface casing shall be tested before drilling the plug by applying a minimum pump pressure as set forth in Table 1 after at least 200 feet of the mud-laden fluid has been displaced with water at the top of the column. If at the end of 30 minutes the pressure gauge shows a drop of 10 percent of test pressure as outlined in Table 1, the operator shall be required to take such corrective measures as will insure that such surface casing will hold said pressure for 30 minutes without a drop of more than 10 percent of the test pressure…”- LAC 43:XIX.109.B.2
After 30 minutes:
<10% decline in
test pressure

## Slide 113
Table 2 |  | 
String Pressure Depth Set | Number of Sacks Cement | Producing Test (lbs. Per sq. in.)
2000-3000’ | 200 * | 800
3000-6000’ | 300 " | 1000
6000-9000’ | 500 " | 1200
9000-Deeper | 500 " | 1500
*But in every case no less cement shall be used than the calculated amount necessary to fill the annular space to a point 500 feet above the shoe. |  | 
Casing Program Requirements – Production Casing Cementing
“Cement shall be by the pump-and-plug method, or another method approved by the department. Sufficient cement shall be used to fill the calculated annular space behind the casing to such a point, as in the opinion of the district manager, local conditions require to protect the producing formations and all other oil and gas formations occurring above, but in every case, no less cement shall be used than the calculated amount necessary to fill the annular space to a point 500 feet above the shoe.”- LAC 43:XIX.109.D.3
≥24 Hour Total Standing Time
Including
≥12 Hour Standing Time Under Pressure
“Cement shall be allowed to stand a minimum of 12 hours under pressure and a minimum total of 24 hours before initiating test or drill plug in the producing or oil string. Under pressure is complied with if one or more float valves are employed and are shown to be holding the cement in place, or when other means of holding pressure is used. When an operator elects to perforate and squeeze or to cement around the shoe, he may proceed with such work after 12 hours have elapsed after placing the first cement.” - LAC 43:XIX.109.D.5
“The amount of cement to be left remaining in the casing…shall be not less than 20 feet. This shall be accomplished through the use of a float-collar, or other approved or practicable means, unless a full-hole cementer, or its equivalent, is used.” - LAC 43:XIX.109.D.4

## Slide 114
Casing Program Requirements - Production Casing Pressure Testing
“Before drilling the plug in the producing string of casing, the casing shall be tested by pump pressure, as determined from Table 2 hereof, after 200 feet of mud-laden fluid in the casing has been displaced by water at the top of the column.” - LAC 43:XIX.109.D.6
After 30 minutes:
<10% decline in
test pressure
Table 2 |  | 
String Pressure Depth Set | Number of Sacks Cement | Producing Test (lbs. Per sq. in.)
2000-3000’ | 200 * | 800
3000-6000’ | 300 " | 1000
6000-9000’ | 500 " | 1200
9000-Deeper | 500 " | 1500
*But in every case no less cement shall be used than the calculated amount necessary to fill the annular space to a point 500 feet above the shoe. |  | 
“If at the end of 30 minutes the pressure gauge shows a drop of 10 percent of the test pressure or more, the operator shall be required to take such corrective measures as will insure that the producing string of casing is so set and cemented that it will hold said pressure for 30 minutes without a drop of more than 10 percent of the test pressure on the gauge.” - LAC 43:XIX.109.D.6.a

## Slide 115
Casing Program Requirements – Casing Test Affidavit
“If the commissioner's agent is not present at the time designated by the operator for inspection of the casing tests of the producing string, the operator shall have such tests witnessed, preferably by an offset operator. An affidavit of test, on the form prescribed by the Department of Conservation, signed by the operator and witness, shall be furnished to the district office of the Department of Conservation showing that the test conformed satisfactorily to the above mentioned regulations before proceeding with the completion…”- LAC 43:XIX.109.D.7

## Slide 116
Regulatory Results of Construction Requirements
Original rules promulgated in 1943 and amended in 1951, 1958, and 1999.
  1999 amendment only addressed conductor casing, tubing and completion.
Well construction of requirements are the same regardless of stimulation method.
Hydraulic fracturing of shallower intervals (Hosston& Cotton Valley) has been common practice for decades.
Well construction requirementsresult in protection of USDW and isolation of hydrocarbon bearing zones.

## Slide 117
Ground Water Resources Program Update

## Slide 118
Mr. Gary Snellgrove
DNR Office of Conservation
Evolution of the Water Well Driller Program
Statewide Water Management Plan
Katrina & Rita Water Well Damage– LRA Funding Update
Haynesville Shale Frac Water Supply Implementation Update
Public Outreach & Education

## Slide 119: Evolution of the Water Well Driller Program
119
Transferred water well driller program from DOTD to DNR
MOU was signed on December 30, 2009 and effective January 1, 2010
Action Items to be completed by March 1, 2010
  Merger of DOTD and DNR databases
  Staffing
  Transfer of files
Notification to DOTD district managers to continue statewide water well inspections
Review, revise, and update water well drillers regulations

## Slide 120
Evolution of the Water Well Driller Program

## Slide 121
Mr. Bo Bolourchi
LA Department of Transportation & Development
State Reservoir Priority and Development Program

## Slide 122: State Reservoir Priority and Development Program Louisiana Ground Water Resources Commission February 3, 2010
Presented by:
Bo Bolourchi, Director, DOTD Public Works & Water Resources
and
Bill McHie, Project Manager, MWH

## Slide 123: Reservoir Priority and Development Program Presentation Outline
RPDP Program Overview
Goals and Objectives
Phase 1 Scope of Work
Phase 1 Deliverables
  Basin Characterization Reports
  Application Process / Guidance
  Reviewer Guidance
  Statewide Perspective
Next Steps – Phase 2

## Slide 124: Program Overview
HB2 of 2007 (Act 28) authorized DOTD to study and produce a Reservoir Priority and Development Program (RPDP)
RFP for Program issued April 4, 2008
MWH contract awarded October 1, 2008 for 2 year time period

## Slide 125: Program Overview (cont)
Program was envisioned to be similar to ongoing Port Priority, Statewide Flood Control and Highway Priority Programs
Program is to establish procedures for submitting applications for reservoir projects, evaluating projects and providing a prioritized list to the Legislature for funding
Program will also provide information about state-wide water resources, including environmental and socioeconomic issues

## Slide 126: Goals and Objectives
Develop a process for evaluating and prioritizing state-funded reservoirs for water supply, flood control, environmental enhancement, socioeconomic development and recreation
Focus on long-term water supply needs and issues
Provide a practical tool for applicants, agencies and State decision makers to facilitate funding of proposed reservoirs
Provide sound scientific and economic criteria for evaluating projects, utilizing best available practices from Louisiana and other states

## Slide 127: Goals and Objectives (cont.)
Develop a priority system to encourage development of projects with best solutions in line with State priorities
Provide a high level, easily understood summary of state-wide water resource issues as a basis for evaluating proposed projects and to promote awareness of water resource needs throughout the state
Provide guidance on long-term State water resources management strategies

## Slide 128: RPDP Phase 1 - Scope of Work
Task 1 - Basin Characterization
Task 2 - Water Resource Needs Assessment
Task 3 - State and Federal Programs Impact Assessment
Task 4 - Reservoir Project Evaluation, Scoring and Prioritization Process
Task 5 - Project Application Guidelines
Task 6 - Project Reviewer Guidelines
Task 7 - Statewide Water Resources Perspective
Task 8 - Ground and Surface Water Modeling, if necessary

## Slide 129: Agencies Participating in Development of RPDP
Louisiana Geological Survey (LGS) | U.S. Geological Survey (USGS)
Louisiana Department of Culture, Recreation and Tourism Division of Historic Preservation | Louisiana Department of Environmental Quality (DEQ)
Louisiana Department of Health and Hospitals – Office of Public Health (DHH) | Louisiana Department of Economic Development (DED)
Louisiana Department of Wildlife and Fisheries (LDWF) | Louisiana Department of Natural Resources (DNR)
Louisiana Department of Agriculture and Forestry (LDAF) | U.S. Department of Agriculture, (NRCS)
U.S. Army Corps of Engineers (USACE) | U.S. Fish and Wildlife Service (FWS)

## Slide 130: Basin Characterization Report Objectives
  Information for applicants
  Resource for the State
  Consistent source of data for review of applications
  Identify issues unique to each basin
  Needs assessment

## Slide 131: Major Surface Water Basins

## Slide 132: Basin Characterization Reports
Basin Overview
Land Use and Legal Entities
Physiographic and Climatic Information
Water Use
Surface Water
Groundwater
Flooding
Environmental and Cultural Issues
Recreation, Navigation and Hydropower
Interbasin and Interstate Issues
Summary of Water Resources Needs

## Slide 133: Two-Phase Application Process
Phase 1 Applications
  Application for study funds (seed money)
  Review initial project descriptions
  Receive input from State and Federal agencies
  Provide guidance to applicant on project feasibility
Phase 2 Applications – Quantitative Ranking
  Application for design and construction funds
  Detailed evaluation and scoring by advisory committee for prioritization for Legislature*
  Note: The role of the evaluation committee is prioritization, not selection

## Slide 134: Applicant Guidance Document
Procedures and Schedules
Instructions for Applicants
Sample Cost and Benefit Calculations
Reference Information Tables
Application Forms

## Slide 135: Reviewer Guidance Document
Background Program Information
Evaluation and Scoring Guidance
Information on Permitting Requirements
Reservoir Feasibility Evaluation Model
Review Worksheets

## Slide 136: LA Statewide Perspective on Water Resources
Summary of water resource uses and issues at a state-wide level such as
  Areas of groundwater concern
  Areas of changing water demand
  Declining water quality
Strategies for water resource management such as
  Water supply advocacy program
  Regional water planning and management

## Slide 137: Phase 1 Status
All Phase 1 work completed
Final review of work products to be completed in February 2010.
Final Deliverables include:
  Executive Summary
  Nine Basin Characterization Reports
  Applicant Guidance Document
  Reviewer Guidance Document
  Statewide Perspective on Water Resources Report

## Slide 138: Phase 2 - Next Steps in RPDP Development
Program Implementation
Pilot testing of process with sample project
Input from potential applicants, professional community and other stakeholders
Presentations to promote the Program
Workshops to explain the process and provide examples

## Slide 139: Phase 2 - Next Steps in RPDP Development
Additional Technical Studies (at select locations and as needed)
Estimate sustainable yields of streams, reservoirs and lakes
Quantify stream flood characteristics
Develop ground and surface water models
Considerations for Phase 2:
Funding
Coordination with DNR Ground Water Management Plan

## Slide 140
    Questions:
QUESTIONS ?

## Slide 141: Statewide Ground Water Management Plan
Timeline
Months 1 & 2
RFP Advertisement,
Receipt & Evaluation
Months 3-7
Award Contract
Contract execution (ongoing)
Month 8
Issue Draft Comprehensive Report and Receive Public Comment
Months 9 - 11 Publish FINAL REPORT
Research, Evaluate, Study, Compile statistics, Identify best management practices, Prioritize, Outreach

## Slide 142
Statewide Ground Water Management Plan

## Slide 143
Dr. Mohan Menon
Ecology & Environment, Inc.
Statewide Ground Water Management Plan

## Slide 144
ecology and
environment, inc.
International Specialists in the Environment

## Slide 145: Statewide Ground Water Management Plan- Outline
Introduction
Objectives and Goals
Technical Approach
Project Schedule
Project Organization

## Slide 146: E&E Corporate Summary
Founded 1970
23 Nationwide Offices
25 Global Affiliates/Offices
Over 1,000 Personnel
75 Professional Disciplines

## Slide 147: Introduction and Background
“Statewide Ground Water Management Plan” -2215-10-04; funded by DHH
Assistance in Developing the Statewide Water Management Plan in 2002
Act 49 of the 2003 L.S. addressed surface and ground water management and conservation
Act 49 mandated development of “Statewide Ground Water Resources Management Program” to evaluate
  Current and projected demand
  Water use conservation program
  Alternatives to ground water use
  Incentives for conservation
  Alternative technologies
  Education and conservation programs
This plan will address this Program
Notes: Notes:

## Slide 148: E&E and the Team
The Team
  Ecology and Environment, Inc. (E&E)
    Experience in Louisiana
    Has successful template for the water resource planning process
    National and International experts in water resource planning
  Louisiana Geological Survey (LGS)
    State’s premier water resource institution
    Conducted multitude of research studies and has access to critical data
  Intera, Inc. (Intera)
    Leading water management planning firm with recent experience in Texas- Statewide Water Plan
The team brings in
  Local knowledge of Louisiana and adjoining water resources
  Experience in similar water planning programs
  Out-of-the-box, innovative thinking
  Integrated multi-disciplinary approach
Notes: Notes:

## Slide 149: Objectives and Goals
Plan for judicious and sustainable use of water resources
Update the baseline conditions of resources and needs
Develop cost-effective water resources alternatives
The plan will address
  Reviewing and modifying the current system of water use reporting and monitoring
  Developing more streamlined ground water well permitting process
  Developing cost-effective alternatives to ground water
  Developing a net work of aquifers to be used in a sustainable manner
  Development or modification of GIS based database management
  Consistency with State’s Master Plan for coastal restoration and protection
  Overarching goal is to develop a plan that is consistent with the State’s vision to preserve the quality and sustainability of its water resources
Notes: Notes:

## Slide 150: Technical Approach
The project will be implemented by executing nine (9) tasks:
  Review of historic and current available information
  Water use analysis
  Review of ground water well prior notification and evaluation procedures
  Feasibility and recommendations for short term (5 year) and long term (25 year) ground water use
  Cost benefit analysis and prioritization of alternatives
  Funding opportunities
  Best management practices and tax incentives
  Public hearing
  Report Preparation

## Slide 151: Task 1: Review of Existing Data
Existing source and use data will be reviewed
USGS, institutions, and universities' resources will be utilized
Information will be packaged into a synopsis by region and water sources
Will consider impacts of subsidence and hence relative sea level rise
Waters do not recognize political boundaries, hence the whole system analysis approach will be used

## Slide 152: Task 2: Water Resources Use Analysis
Analysis will use:
Pertinent data from Task 1
Historic and current trends for population growth and movement
Historic and projected water demands by population and various other sectors
Data gaps will be indentified and recommendations will be made for parishes and local entities to monitor such vital statistics

## Slide 153: Task 3: Review of Ground Water Well Prior Notification Procedure
Current procedures will be reviewed upon receipt, review, and evaluation phases
Recommendations will be made to streamline the process and to evolve better approach to understand or estimate the current demands on the aquifers
Opportunities for data base evaluation and on-line data entry for increasing efficiency and accuracywill be evaluated

## Slide 154: Task 4: Feasibility Study…
Will use ground water availability models (existing)
Maps (region/aquifer scale) for
  Areas of water decline, areas of salt water intrusion, potential alternate sources
Sustainability and water quality objectives
  Water use reduction strategies, water and waste water recycling, mitigation measures
Recommendations will be based on
  Areas of greatest stress
  Water use trends in proposed service areas
  Demographic projections
  Inhibition of salt water intrusion
  Unit cost for water treatment
  Preservation of the aquifers
  Education and awareness

## Slide 155: Task 4: ….Short (5 yr) and Long (25 yr) Term Alternatives
Plan may recommend development or modification of existing availability models
Cost-benefit analysis for proposed alternatives will be consistent with DED methods to identify viable alternatives
Recommendations will include development of ground water level and water quality monitoring program

## Slide 156: Task 4: ….Financial Feasibility Analysis
Financial feasibility of alternatives to current ground water production
Cost/benefit ratios
Prioritization of short and long term alternatives
Elements of Financial Feasibility Analysis
  Calculate complete life cycle cost of each alternative (initial capital costs, O&M, and replacement costs)
  The costs and revenues will be calculated by comparing the situation with and without the alternatives

## Slide 157: Task 4: … Financial Feasibility Analysis..
Each alternative will be compared against the information on potential local, state, and Federal funding sources (Task 6). Prioritization of the alternatives will depend on the availability of funding
To assess the financial feasibility of each alternative, the Financial Internal Rate of Return (FIRR) will be compared to the Weighted Average Cost of Capital (WACC)
Financial analyses will be conducted in real terms (inflation adjusted) in line with standard practices

## Slide 158: Task 4: …Uncertainty Analysis
Base case assumptions (anticipated likely values) and actual cost and revenue values will be evaluated
Sensitivity and risk analysis will be conducted for each alternative as part of the uncertainty analysis

## Slide 159: Task 5: Cost-Benefit Analysis and Prioritization
Relationship between differing ground water output (alternatives) and their estimated costs will be determined
Estimate of each alternative’s cost with its estimated output (benefit), its Average Incremental Cost (AIC) can be calculated
Supply curve will be created showing the amounts and costs of water supplied by alternative sources
A list of short and long term alternatives will be developed based on financial feasibility, sensitivity, risk, cost-benefit ratio, other factors (including DED methods)

## Slide 160: Task 6: Funding Opportunities
Federal, State, and local funding sources will be explored
Funding sources may be explored for:
  Water treatment
  Transmission
  Distribution and storage for surface water supplies
  Reclaimed water processing and reuse
  Other

## Slide 161: Task 6: Funding Opportunities…
Funds that are targeted towards achieving water conservation include:
  Build America Bonds (BABs)
  WRDA 1992 funds (Environmental Infrastructure)
Potential Funding Sources, examples:
  USDA/Rural Utility Service Grants
  DHH/EPA/LDEQ
  Louisiana Capital Outlay Program
  Louisiana CDBG
  Clean Water State Revolving Funds
  And many others

## Slide 162: Task 6: Funding Opportunities…
Innovative programs will be evaluated such as:
  Water Independence Now (WIN) program
  New South Wales, Australia, State Ground Water Policy
  Texas ground water conservation district rules and permitting programs
  Ground water replenishment program, etc.

## Slide 163: Task 7: BMPs and Tax Incentives
Best Management Practices (nationwide, state, and regional) for tax incentives to reduce the cost for implementing management measures
  Some incentives are designed to encourage private sector participation
  Tax incentives relating to promoting conservation and water reuse
  Popular nationwide programs will be explored
Focus will be on incentives that balances fiscal considerations, efficiency, and environmental concerns
Intense water use sectors will be targeted first

## Slide 164: Task 8: Public Hearing
Four (4) public hearings will be facilitated
Presentations will focus on technical and scientific approach for the water management
Goals of these hearings:
  Introduction of projects and processes
  Build relationships and conflict resolution
  Identify stakeholder issues and concerns, and opportunities

## Slide 165: Task 9: Draft and Final Report
Draft report of findings will be submitted to LDNR for their input and comments
Public comments will be received and incorporated
An executive summary and final report will be prepared

## Slide 166: Project Schedule

## Slide 167: Project Organization

## Slide 168
ecology and
environment, inc.
International Specialists in the Environment

## Slide 169: Hurricanes Katrina & Rita Water Well Damage Assessment
Ongoing discussions with LRA for funds to cover damaged well p&a / repair costs
Appears to be an eligible expense
Currently seeking unallocated funding sources

## Slide 170: Haynesville Shale Frac Water Mandatory Drilling &Frac Water Supply Source and Volume Reporting

## Slide 171
Haynesville Shale Frac Water
Mandatory Drilling &Frac Water Supply Source and Volume Reporting
Actions of the Commissioner:
Requires operators to report water sources and volumes
Issued on September 15, 2009
Enforceable effective October 1, 2009
Provides valuable ground water resource management tool
Statistics

## Slide 172
Haynesville Shale Natural Gas Well Development
Drilling and Stimulation Operations
Reported Water Usage from 10/1/2009 to 1/22/10 WH-1 Information
Source | Volume (Gallons)
Frac Groundwater | 21,460,073
Frac Surface Water | 125,579,242
Drilling Rig Groundwater | 26,980,766
Drilling Rig Surface Water | 1,020,000
Other Groundwater | 105,000
Other Surface Water | 1,281,000
Chart: 
| Drilling Rig Supply Groundwater Volume (Gallons) | Drilling Rig Supply Surface Water Volume (Gallons) | Frac Groundwater Volume (gallons) | Frac Surface Water Volume (gallons) | Other Groundwater | Other Surface Water
 | 26980766 | 1020000 | 21460073 | 125579242 | 105000 | 1281000

## Slide 173
Haynesville Shale Frac Water
Domestic Well Water Use For Non-Domestic Purposes
Provides regulatory clarification
Requires Prior Notification & Evaluation

## Slide 174: Statewide Well Notification Audit and Enforcement
January | February | March | April | May | June | July | August | September | October | November | December
Caddo, Red River, Bossier, DeSoto |  |  |  |  | Calcasieu, Cameron | Jeff Davis, Vermillion | Acadia, Lafayette | Allen, Evangeline, St. Landry | Bienville, Webster | Claiborne, Jackson, Lincoln | Ouachita, Morehouse, Union
CARIZZO – WILCOX (Haynesville) |  |  |  |  | CHICOT |  |  |  | SPARTA |  | 
Initiated a comprehensive statewide audit schedule
  Two year plan to audit all ground water wells drilled in Louisiana after July 1, 2001
  To date,21 parishes audited
  Current status of implementation
2009 Schedule

## Slide 175
January | February | March | April | May | June | July | August | September | October | November | December
Bienville, Bossier, Caddo, Desoto, Red River, Webster | Claiborne, Jackson, Lincoln, Morehouse, Ouachita, Union | Acadia, Calcasieu, Cameron, Jeff Davis, Vermillion | Allen, Beauregard, Evangeline, Lafayette, St. Landry | EBR, E. Feliciana, Livingston, St. Helena, WBR, W. Feliciana | E. Carroll, Franklin, Madison, Richland, Tensas, W. Carroll | Caldwell, Grant, LaSalle, Natchitoches, Sabine, Winn | Avoyelles, Catahoula, Concordia, Rapides, Vernon | Assumption, Iberia, Iberville, Pointe Coupee, St. Martin | Ascension, St. Charles, St. James, St. John, Tangipahoa, Washington | Orleans, St.Tammany | Jefferson, Lafourche, Plaquemines, St. Bernard, St. Mary, Terrebonne
Comprehensive statewide audit schedule continued…
January | February | March | April | May | June | July | August | September | October | November | December
EBR, E. Feliciana, WBR, W. Feliciana | Livingston, St. Helena, Tangipahoa, Washington | St. Tammany | E. Carroll, Madison, Richland, W. Carroll | Catahoula, Concordia, Franklin, Tensas | Caldwell, Grant, LaSalle, Natchitoches, Sabine, Winn | Beauregard, Vernon | Avoyelles, Pointe Coupee, Rapides | Assumption, Iberia, Iberville, St. Martin, St. Mary | Ascension, St. Charles, St. James, St. John | Jefferson, Lafourche, Terrebonne | Orleans, Plaquemines St. Bernard
SOUTHEAST LOUISIANA |  |  | MS RIVER ALLUVIAL |  | OTHER |  |  |  |  |  | 
2010 Schedule
Annual Statewide Schedule - Beginning 2011 and proceeding annually
Statewide Well Notification Audit and Enforcement

## Slide 176: Statewide Well Notification Audit and Enforcement Results
Parish Actions
Caddo 71
Red River 28
Bossier 65
DeSoto 53
Calcasieu 83
Cameron 24
Jefferson Davis 88
Vermilion 161
Acadia 114
ParishActions
Lafayette 91
Allen 31
Evangeline 40
St. Landry 95
Bienville 60
Webster 43
Claiborne 33
Jackson 23
Lincoln 47
Ouachita 39
Morehouse 97
Union 27

## Slide 177: Public Outreach & Education
  NRCS / DNR Cooperative Effort
  LSU Ag Center staff education
  Louisiana Ground Water Association Seminar

## Slide 178: Public Outreach & Education Water Well Notification Email Distribution
Provides email notice to 64 parish contacts and other interested parties
  1st email received upon receipt
  2nd email received upon approval

## Slide 179
Mr. Pat Credeur
Executive Director
Louisiana Rural Water Association

## Slide 180: Louisiana Rural Water Association

## Slide 181
Louisiana Rural Water Association (LRWA) is governed by a membership elected board of directors. LRWA is a non-profit organization established in 1978 to assist small water and wastewater systems through training, on-site technical assistance, and state operator certification.

## Slide 182
TRAINING PROGRAM: LRWA takes pride in the Training and Technical Assistance that we offer throughout the year from one end of Louisiana to the other. The Training Sessions are instructed by individuals with a wide variety of expertise in Water and Wastewater related areas, as well as Louisiana Department of Health and Hospitals Office of Public Health personnel to keep attendees abreast of current and changing State Regulations. LRWA offers a wide variety of Training Sessions such as Environmental Protection Agency (EPA), Louisiana Compliance Initiative (LCI), Very Small Water System (VSWS), Wastewater, and Board/Council Member as well as our Annual Conference which includes Certification Training and Technical Training for office personnel.

## Slide 183
SIntroduction to Safe Drinking Water Program
SEnforcement, How to Maintain Compliance
SBacteriological Sampling
SOperator Certification Program
SGroundwater Protection Program
SOperating a water system…Getting Certified
SSewer Lift stations
STroubleshooting, Control Transformers, Single Phase
SSmoke Testing and TV Inspections
SHydrant Operations
SDisinfection Challenges and Chlorine Safety
STroubleshooting Filters
SWater Leak Detection
SWastewater Plant Operations
SElectrical Equipment
SEverything You Need to Know About Chlorinators
SCross-Connections
SProper Security for your Water System
SSecurity Vulnerability/Emergency Response Plan
Training Topics

## Slide 184: Training Sessions provide Continuing Education Units (CEU)
We provide training sessions throughout the state in order to help operators maintain their level of certification that is required by the LA Dept. of Health & Hospitals. We offer topics on water & wastewater as it relates to the workforce in today’s environment.

## Slide 185: Annual Conference
CONFERENCE: LRWA provides an Annual Conference to over 1,500 water and wastewater professionals, as well as mayors, board members, clerks, and decision makers. This conference allows these professionals to receive expert training, as well as receiving up to 32 hours of re-certification credits. This conference has had over 120 exhibitors displaying their state of the art products, which is important to the water and wastewater industry. Our annual conference puts water and wastewater personnel in touch with vendor’s products while obtaining valuable training.

## Slide 186: Exhibit Booths & Awards

## Slide 187: USDA

## Slide 188: EPA

## Slide 189: State Programs

## Slide 190: On-Site Technical Assistance
Water & Wastewater on-site assistance
Smoke testing, leak detection, sewer video camera
Rate structures
Well drawdown
Hydrant flushing

## Slide 191: Lend a willing hand
LRWA staff visit systems to provide expert advice and offer solutions to problem areas with water and wastewater systems.

## Slide 192
Next Meeting Date
Wednesday, April 7, 2010
11:00 AM
Baton Rouge, LA